Complex coacervation of gelatin and OSA-modified kudzu starch

Y Zhao 1, N Khalid 3, M A Neves 1, 2, 4, I Kobayashi 2, 4, M Nakajima 1, 2, 4

1 Graduate School of Life and Environmental Sciences, University of Tsukuba, 1-1-1 Tennoudai, Tsukuba, Ibaraki 305-8572, Japan

2 Tsukuba Life Science Innovation Program (TLSI), University of Tsukuba, 1-1-1 Tennodai, Tsukuba, Ibaraki 305-8572, Japan

3 School of Food and Agricultural Sciences, University of Management and Technology, Lahore 54000, Pakistan

4 Food Research Institute, NARO, 2-1-12 Kannondai, Tsukuba, Ibaraki 305-8642, Japan

Kudzu (Pueraria lobata) starch is an important traditional food and used as natural medicine in different Asian countries due to its smooth texture after gelatinization and small amounts of isoflavonoids [1,2]. In this study, kudzu starch granules were modified using octenyl succinic anhydrate (OSA) to formulate complex coacervates with gelatin (type A, from porcine skin). Moreover, the physicochemical properties of OSA-modified kudzu starch and its formulation of coacervates were also investigated. The viscosity of OSA-modified kudzu starch suspension increased after gelatinization, together with granule size. The addition of bifunctional groups decreased the interfacial tension between soybean oil and gelatinized OSA-modified kudzu starch in comparison to native kudzu starch. The efficiency of oil droplet disruption during homogenization was dependent on the oil-water interfacial tension [3], therefore the produced droplet size of O/W emulsions stabilized by gelatinized OSA-modified kudzu starch was decreased, and its emulsifying ability was enhanced after modification. The optimized conditions for coacervation included mixing of gelatin and OSA-modified kudzu starch in a ratio of 1:1 (w/w) at an optimized pH of 6. The results of this study showed that kudzu starch granules could be modified with OSA. Moreover, the gelatinized modified kudzu starch could be used as food-grade emulsifier or new wall materials for microencapsulation of sensitive bioactives.

References:

1	Hung, V. P., Morita, N. (2007). Chemical compositions, fine structure and physicochemical properties of kudzu (Pueraria lobata) starches from different regions. Food Chemistry, 105, 749-755.

2	Wong, K. H., Li, G. Q., Li, K. M., Razmovski-Naumovski, V., Chan, K. (2011). Kudzu roo: traditional uses and potential medicinal benefits in diabetes and cardiovascular diseases. Journal of Ethnopharmacology, 134, 584-607.

3 Cheng, Q., McClements, D. J., (2011). Formation of nanoemulsions stabilized by model food-grade emulsifiers using high-pressure homogenization: Factors affecting particle size. Food Hydrocolloids, 25, 1000-1008